## Slide 1
Analysing Factors Affecting Nitrogen Oxides (NOx) Emissions of Gas Turbine
Submitted To :
Prof. Devlina Chatterjee HOD-DoMS, IIT Kanpur
Sr. No | Students Name | Enroll. No
1) | Ankit Kumar | 251140002
2) | Nikhil D. Madankar | 251140014
3) | Sameer Saurav | 251140021
4) | Subodh Singh | 251140024
Course Title : Statistical Modeling for Business Analytics
Course Code : MBA652
Group 13

## Slide 2
Contents
Objective & Background
Data Source & Variables
Descriptive Statistics & Outlier Removal
Scatterplot Analysis
Correlation Matrix
Full Model & Multicollinearity (VIF)
Model Comparison (Backward Elimination)
Final Model & Interpretation
Conclusion

## Slide 3
Objective & Background
Objective
To analyze operational and environmental factors affecting NOx emissions of an industrial gas turbine, and build a multiple linear regression model to predict emission levels for environmental compliance and process optimization.
Background
Peak combustion flame temperatures trigger thermal NOx formation — a pollutant under strict emission ceilings.
Predicting NOx from standard sensor telemetry supports continuous compliance verification, combustion-anomaly detection, and a computational proxy when physical CEMS units are under maintenance.
NOx escapes into the sky and creates smog and acid rain, Coughing .

## Slide 4
Data Source & Variables
Dataset: Gas Turbine CO and NOx Emission Data Set (2011-2015), UCI ML Repository Source: Operating cogeneration gas turbine, north-western Turkey (SCADA logging) Contact: heydarkaya@nku.edu.tr, ptufekci@nku.edu.tr, euzun@nku.edu.tr Sample: 36,733 hourly records → 35,347 after z-score outlier removal (|z| ≤ 3)
Variable | Description | Unit
NOx (Y) | Nitrogen oxides emissions | mg/m³
AT | Ambient temperature | °C
AP | Ambient pressure | mbar
AH | Ambient relative humidity | %
AFDP | Air filter differential pressure | mbar
GTEP | Gas turbine exhaust pressure | mbar
TIT | Turbine inlet temperature | °C
TAT | Turbine after temperature | °C
TEY | Turbine energy yield (power output) | MWh
CDP | Compressor discharge pressure | mbar

## Slide 5
Industrial Gas Turbine Components
AI Generated Picture for Better Understanding of Variables

## Slide 6
Descriptive Statistics

## Slide 7
Descriptive Statistics & Outlier Removal
Method:
Standardized z-score, observation dropped if any of 10 variables had |z| > 3
N before: 36,733 → N removed: 1,386 → N after: 35,347
NOx std dev falls from 11.68 to 10.43 without materially shifting the mean (65.3 → 64.55).
TIT and TAT cluster near their upper limits — turbine spends most of its time near full-load operating temperatures.

## Slide 8
Scatterplot Analysis
Why the NOx emission decreases with increase in AT ? When the outside air becomes hotter . Hot air is less dense. That changes the amount of air the compressor can ingest for a given operating condition and affects turbine performance, load, air–fuel ratio, compressor operation, etc.
NOx and Ambient temperature (AT) has strongly negative relation
NOx vs Ambient Pressure (AP) Relationship: Weak positive
NOx vs Ambient Humidity (AH) Relationship: Weak positive
TIT and TEY doesn't show a strong linear relationship with NOx

## Slide 9
Correlation Matrix
Implication: This is preliminary evidence of severe multicollinearity — confirmed formally via VIF (Variance Inflation Factor)
Pair | Correlation
GTEP – TIT | 0.88
GTEP – TEY | 0.96
GTEP – CDP | 0.98
TIT – TEY | 0.92
TIT – CDP | 0.92
TEY – CDP | 0.99
TAT – TEY | −0.72
TAT – CDP | −0.74

## Slide 10
Full Model (9 Predictors) & Multicollinearity
R² = 0.551 Adj. R² = 0.546 , p < 0.001
Predictor | Coef | p-value | VIF
AT | -1.671 | <0.001 | 8.3
AP | -0.225 | <0.001 | 1.5
AH | -0.214 | <0.001 | 1.6
AFDP | 0.908 | <0.001 | 2.4
GTEP | 0.082 | 0.094 | 28.5
TIT | 1.418 | <0.001 | 35.1
TAT | -1.348 | <0.001 | 9.0
TEY | -1.571 | <0.001 | 246.6
CDP | -6.419 | <0.001 | 238.1
Model 1 : NOx = β₀ + β₁AT + β₂AP + β₃AH + β₄AFDP + β₅GTEP + β₆TIT + β₇TAT + β₈TEY + β₉CDP + ε
The full model explains about 55.1% of the variation in NOx emissions
However, severe multicollinearity exists among turbine-load variables, especially TEY (VIF 246.6) and CDP (VIF 238.1) are essentially redundant , while GTEP is insignificant (p = 0.094)
A VIF above 10 is commonly considered an indication of serious multicollinearity

## Slide 11
Model Comparison (Backward Elimination)
Model 4 is retained as final:
- TEY, CDP and GTEP were removed due to high multicollinearity and/or insignificance.
- After removing them, all VIF values fell below 2.4, indicating no serious multicollinearity.
Model | Variables Included | Dropped | Reason | R² | Adj. R²
Model 1 | All 9 predictors | None | Full baseline | 0.551 | 0.546
Model 2 | 8 (drop TEY) | TEY | Severe Collinearity ( VIF = 246.6 ) | 0.5308 | 0.5303
Model 3 | 7 (drop CDP) | CDP | Severe Collinearity ( VIF = 87.2 ) | 0.3709 | 0.3708
Model 4 | 6 (drop GTEP) | GTEP | Insignificant ( p = 0.094 & VIF = 13.2 ) | 0.3708 | 0.3707
NOx= −176.13−1.67AT−0.225AP−0.214AH+0.908AFDP+0.082GTEP+1.418TIT−1.348TAT−1.571TEY−6.419CDP
NOx= 51.501−1.158AT−0.136AP−0.209AH+1.186AFDP−0.342GTEP+1.167TIT−1.429TAT−23.995CDP
NOx= 173.252−1.118AT−0.224AP−0.214AH+1.258AFDP−2.835GTEP+0.464TIT−0.511TAT
NOx= 90.089−1.120AT−0.146AP−0.155AH+1.861AFDP−0.013TIT+0.295TAT

## Slide 12
Final Model & Interpretation
NOx = 90.09 − 1.12·AT − 0.146·AP − 0.155·AH + 1.861·AFDP − 0.013·TIT + 0.295·TAT
R² = 0.3708 Adj. R² = 0.3707 , p < 0.001 | All VIF < 2.4 (no multicollinearity)
AT (−1.12)
Higher ambient temperature is associated with lower NOx emissions.
AH (−0.15)
Humidity dilutes combustion, lowering peak flame temperature — suppresses NOx.
AFDP (+1.86)
Largest-magnitude effect. Higher air-filter pressure is associated with higher NOx emissions.
TAT (+0.30)
Hotter exhaust-side temperature, holding inlet fixed, indexes a hotter combustion cycle.

## Slide 13
Implications & Practical Applications for Regulators (India)
Localized Microclimate Mitigation & Urban Greening:
  Since ambient temperature () heavily influences emissions and thermal dynamics, mandatory green-belt policies and urban forestry around industrial clusters should be implemented to mitigate the Urban Heat Island (UHI) effect.
Dynamic Environmental Compliance & Temperature-Based Standards:
  Environmental regulators should consider shifting from static emission norms to dynamic standards that account for seasonal ambient temperature fluctuations, which alter thermal efficiency and emission behaviors.

## Slide 14
Conclusion
1
Ambient temperature (AT) is the strong predictor of NOx and explaining large of its variance.
2
The turbine “load” process variables (GTEP, TIT, TAT, TEY, CDP) are severely inter-correlated (|r| up to 0.99); dropping TEY, CDP and GTEP resolves it.
3
4
The final model explains 37.1% of NOx variance (Adj. R²), with inference accounting for confirmed heteroskedasticity .
5
Cooler, drier ambient air and a hotter restricted combustion process are all associated with higher NOx emissions.
Forward selection and VIF-driven elimination independently converge on the same 6-variable model: AT, AP, AH, AFDP, TIT, TAT.

## Slide 15
Appendix

## Slide 16
Appendix

## Slide 17
Appendix

## Slide 18
OLS Regression Results

## Slide 19
OLS Regression Results

## Slide 20
Key Formulas

## Slide 21
Thank You!